## Slide 1
IBK412: Environmental Bioprocess Technology
By
Muaz bin Mohd Zaini Makhtar
Email: muazzaini@usm.my ANNEX Building, Room A401
1

## Slide 2: Guys, Your Agenda Layout
01
Quiz
02
Quiz
03
Quiz
04
Quiz
05
Quiz

## Slide 3
Any question regarding all this quizzes..?
Section Break

## Slide 4
Welcome 4th year!!

## Slide 6: Question from Muaz to all of you: What factors push you to do well in your life?

## Slide 7: As you were at primary & secondary school, share Three (3) factors motivated you the most. Go to www.menti.com and use the code 33 63 164

## Slide 8: Free ads

## Slide 9: While currently, at USM, share THREE (3) factors motivated you the most. Go to www.menti.com and use the code 33 63 164

## Slide 12: Wastewater
Sewage is a water-carried waste, in solution or suspension, that is intended to be removed from a community. Also known as wastewater, it is more than 99% water and is characterized by volume or rate of flow, physical condition, chemical constituents and the bacteriological organisms that it contains.
Sewerage is the physical infrastructure, including pipes, pumps, screens, channels etc. used to convey sewage from its origin to the point of eventual treatment or disposal. It is found in all types of sewage treatment, with the exception of septic systems, which treat sewage on site

## Slide 13: Wastewater
Wastewater Treatment
Wastewater is the water used by a community
Collected and treated prior to discharge
Standards of treatment vary but are generally becoming more stringent
Treatment is a process of removal of smaller and smaller particles

## Slide 14: Wastewater Treatment Flow
Sludge disposal
Tertiary
Secondary
Primary
Preliminary
Pretreatment
Go to www.menti.com and use the code 33 63 164

## Slide 15: Bacteria
16
Bacteria at sewage can be classified according to the roles . Some bacteria perform positive roles in the treatment of wastewater, while other bacteria perform negative roles that contribute.
Acetongenic bacteria
Coliforms
Cyanobacteria
Denitrifying bacteria
Fecal coliforms
Fermentative (acid-forming) bacteria
Filamentous bacteria
Floc-forming bacteria
Gliding bacteria
Gram-negative aerobic cocci and rods
Gram-negative facultative anaerobic rods
Hydrolytic bacteria
Methane-forming bacteria
Nitrifying bacteria
Nocardioforms
Pathogenic bacteria
Poly-P bacteria
Saprophytic bacteria
Sheathed bacteria
Spirochetes
Sulfur-oxidizing bacteria
Sulfur-reducing bacteria
Signifcant groups of bacteria

## Slide 16
21
Bacteria
Acetogenic Bacteria (Example: Acetobacter)
Members of the Acetobacteracae family produce acetate (CH3COOH) .They are important in the degradation of soluble BOD to methane in anaerobic digesters. They are a special group of fermentative bacteria and convert organic acids, alcohols, and ketones to acetate, carbon dioxide, and hydrogen .Acetate is the principle substrate used by methane-forming bacteria for the production of methane (CH4). Important acetogenic bacteria include Acetobacter, Syntrobacter, and Syntrophomonas.

## Slide 17
21
Bacteria
Coliforms (Example: Escherichia)
Members of the coliform group of bacteria are Gram-negative rods that ferment the sugar lactose at 37°C and produce gas. The total coliform group includes these genera of the Enterobacteriacease family: Citrobacter, Enterobacter, Escherichia, Hafnia, Klebisella, Serratia, and Yersinai.
Denitrifying Bacteria (Example: Bacillus)
Denitrifying bacteria are facultative anaerobic bacteria that use nitrate (NO3 − ) in the absence of free molecular oxygen to degrade soluble BOD. The use of nitrate results in the return of nitrogen to the atmosphere as molecular nitrogen (N2) and nitrous oxide (N2O). Denitrification is used to satisfy a total nitrogen discharge requirement for a wastewater treatment plant. The most species of denitrifying bacteria are Alcaligenes, Bacillus, and Pseudomonas.

## Slide 18
21
Bacteria
Fermentative (Acid forming) Bacteria (Example: Proteus)
Fermentative or acid-forming (acidogenic) bacteria convert amino acids, fatty acids, and sugars to organic acids including acetate (CH3COOH), butyrate (CH3CH2CH2COOH), formate (HCOOH), lactate (CH3CHOHCOOH), and propionate (CH3CH2COOH). Fermentative bacteria are important in anaerobic digesters where they convert complex substrates to simple substrates that can be used by methane- forming bacteria. There are numerous of fermentative bacteria: Bacteroides, Bifidobacteria, Clostridium, Escherichia, Lactobacillus, and Proteus.

## Slide 19
21
Bacteria
Floc-Forming Bacteria (Example: Zoogloea)
Their roles are in the activated sludge process, which increasing sludge age and produce the necessary cellular components needed to stick together , and include Achromobacter, Aerobacter, Citromonas, Flavobacterium, Pseudomonas, and Zoogloea.

## Slide 20
23
Bacteria
Filamentous Bacteria (Example: Haliscomenobacter)
The organisms that contribute to settleability problems in activated sludge processes due to their rapid and undesired growth and are responsible for most bulking episodes, also due to contribute the degradation of soluble cBOD and floc formation.The most commonly bacteria are Haliscomenobacter , Microthrix, Nocardioforms, Sphaerotilus, Thiothrix, type 0041, type 0092, type 0675, type 1701, and type 021N.

## Slide 21
23
Bacteria
Gliding Bacteria (Example: Beggiatoa)
There are three motile or gliding filamentous organisms in the activated sludge process that contribute to settleability problems. These organisms are Beggiatoa, Flexibacter, and Thiothrix

## Slide 22
23
Bacteria
Gram-Negative, Aerobic Cocci and Rods (Example: Acetobacter))
They make up approximately 20% of the bacteria in the activated sludge process. They are involved in biological phosphorus removal, degradation of soluble BOD, floc formation, and nitrification. Generally include Acetobacter, Acinetobacter, Alcaligens, Nitrobacter, Nitrosomonas, Pseudomonas, and Zoogloea.

## Slide 23
Bacteria
Methane-Forming Bacteria (Example: Methanobacterium)
Methane-forming bacteria or methanogens produce methane (CH4) from a limited number of substrates in anaerobic digesters. Examples of bacteria include Methanobacterium, Methanococcus, Methanomonas, and Methanosarcinia.

## Slide 24
Bacteria
Nitrifying Bacteria (Example: Nitrosomonas)
Nitrifying bacteria are strict aerobes. They oxidize ionized ammonia (NH4 + ) to nitrite (NO2 − ) and oxidize nitrite to nitrate (NO3 − ). Bacteria that oxidize ionized ammonia include Nitrosomonas and Nitrosospira. Bacteria that oxidize nitrite include Nitrobacter and Nitrospira.

## Slide 25
Gram-Negative, Facultative Anaerobic Rods (Example: Escherichia)
They are involved with biological phosphorus removal, acetate production, acid production, degradation of soluble cBOD, denitrification, floc formation, and hydrolysis of BOD ,include Aeromonas, Escherichia, Flavobacterium, Klebsiella, Proteus, and Salmonella.

## Slide 26
Hydrolytic Bacteria (Example: Bacteriodes)
Numerous facultative anaerobic bacteria make up the hydrolytic bacteria. They produce exoenzymes that solubilize complex insoluble substrates into simple soluble substrates and can be absorbed and degraded by larger number of bacteria such as :Bacteroides, Bifidobacteria, and Clostridium.
Poly-P Bacteria (Example: Acinobacter)
Poly-P bacteria or phosphorus accumulating organisms (PAO) are used in biological phosphorus removal units. By recycling the bacteria through anaerobic and aerobic zones, the bacteria remove orthophosphate (H2PO4 −
/HPO4 2− ) from the wastewater in quantities greater than normal cellular needs, include Acinobacter, Aerobacter, Beggiatoa, Enterobacter, and Proteobacter.

## Slide 27
Members of cyanobacteria are photosynthetic bacteria. Before their procaryotic cell structure was recognized, they were considered to be blue- green algae. Cyanobacteria may be found as individual cells (Chlorella) or a chain of cells (Oscillatoria). Some of cyanobacteria occur in the activated sludge process and may contribute to settleability problems. Examples of cyanobacteria include Anabaena, Chlorella, Euglena , and Oscillatoria.
ALGAE-CYANOBACTERIA

## Slide 28: Oscillatoria
Anabaena
Euglena
Chlorella

## Slide 29
Fungi usually are saprophytic organisms and are classified by their mode of reproduction. As saprophytes they obtain their nourishment from the degradation of dead organic matter. Most fungi are free-living and include yeast, molds, and mushrooms. In sewage can find filamentous fungi such as: Pencillium ,Trichoderma and Spicaria .
These are produced phosphate ,an enzyme that release orthrophosphate from phosphorus – containing compounds,which is readily available phosphorous nutrient for bacterial growth and energy transfer.
Yeast The presence of large amounts of yeast in the sewage can indicate a low pH, the existence of fermentative conditions, or a severe phosphorous deficiency. Raising the pH above 7 will usually make the yeast disappear.
FUNGI

## Slide 30: Yeast
Trichoderma
Yeast
Pencillium
Spicaria

## Slide 31
Several types of protozoa such as: amoebae, ciliates, and flagellates are found present throughout the entire sewage water treatment process.
They play a predatory role in removing bacteria, other protozoa, and several small particles.
Larger forms of amoebae eat ciliates and flagellates as well as smaller
amoebae feed primarily on bacteria.
Giardia lamblia is a waterborne pathogen found in sewage water, enters the water supply through contamination by fecal matter. It is aparasite Cryptosporidium is waterborne pathogenic bacterium found in
wastewater.
PROTOZOA

## Slide 32: Amoebea
Giardia
Ciliates
Cryptosporidium
Flagellates

## Slide 33
Enterovirus and rotavirus, are excellent indicators of human fecal contamination in wastewater evident and association with human infections.
viruses can also be found throughout the process of sewage water treatment.
Enteroviruses and rotaviruses are detected in sewage using living cells as hosts due to the fact that viruses are obligate intracellular parasites which need living cells to be able to replicate.
VIRUS