## Slide 1: EKC 464 BIOREFINERY ENGINEERING
Nur Ayshah Rosli, PhD
Room No: 2.22
Ext: 6487

## Slide 2: Learning outcome
Able to list out pre-treatment techniques of biomass using thermochemical methods in biorefineries

## Slide 3: Thermochemical Processing of Biomass
General features, fundamental of design calculation & process design

## Slide 4: Reference
Thermochemical processing of biomass : conversion into fuels, chemicals and power - Edited by Robert C. Brown - Contributor(s): Brown, Robert C. Robert Clinton.
Biorefineries and Chemical Processes: Design, Integration and Sustainability Analysis - Author(s): Jhuma Sadhukhan Kok Siew Ng Elias Martinez Hernandez

## Slide 5: Thermochemical processing
Main biorefinery platforms – biomass is converted into high value intermediate process.
These process extract energy from the carbonaceous materials, transforming carbon, hydrogen and oxygen atoms in the materials into other forms of energy.
Gasification, pyrolysis and combustion.
Intermediate products are subsequently converted into fuel, electricity, and chemicals.

## Slide 7: Methods of biomass conversion
Ref: Lewandowski, W. M., Ryms M., Meler P., Termiczno-chemiczna piroliza do biopaliw ciekáych i gazowych, jako metoda podnoszenia sprawnoĞci konwersji energii biomasy, Nafta-Gaz, Kraków 2010.

## Slide 8
Biomass Thermal Conversion Processes
Combustion
Gasification
Pyrolysis
Heat and Power
Liquids
Fuel gases and syngas
Fishcer-Tropsch Synthesis
Refining
Motor fuels
Motor fuels

## Slide 9
Carbonaceous material
Intermediate product
Final product
Combustion
Gasification
Pyrolysis
Coal
Biomass
Municipal Solid Waste
Steam
SynGas
Pyrolysis Oil
Turbine
Synthesis Reactor
Fuel
Electricity
Chemical

## Slide 10: Advantages of thermochemical processing route
High conversion of feed into products
Feedstock flexibility with acceptance of wide range of biomass
Compatibility with existing facilities using fossil fuel with minimal modification and upgrade
Production yield is stable and large-scale production can be achieved

## Slide 11: Advantages of thermochemical conversion of biomass over biological/biochemical process*
Thermochemical | Biological/biochemical
Effectively applied to almost any biomass feedstock | Involves the use of microbes, enzymes, and/or chemicals to utilize the limited range of biomass
Relatively higher productivity (production per unit time) due to completely chemical nature of reaction | Productivity is limited due to biological conversion. Increase would require higher capital investment such as bigger reactor
Multiple high-value products possible using fractional separation of products | Normally, limited to one or few products and would require additional microbial culture, enzymes for more products
Independent of climate conditions, operates at much higher temperature range, therefore, effect of ambient temperature will be minimal | Mostly susceptible to ambient temperature, and so forth such as anaerobic digester, sunlight for algal ponds
Mostly complete utilization of the waste/biomass | Production of secondary wastes such as biomass sludge
*Verma, M., Godbout, S., Brar, S. K., Solomatnikova, O., Lemay, S. P., & Larouche, J. P. (2012). Biofuels production from biomass by thermochemical conversion technologies. International Journal of Chemical Engineering, 2012.

## Slide 15: Syngas abbreviation for synthesis gas
Made up of carbon monoxide, and hydrogen (85%) with smaller amounts of carbon dioxide and methane.
Has a high calorific value so it can be used as a fuel to generate electricity or steam.
May also be used as a basic chemical in the petrochemical industry.
Has less than half the energy density of natural gas.

## Slide 16: Energy density
Energy density is mount of energy that can be stored in a given mass of a substance or system.
The higher the energy density of a system or material, the greater the amount of energy stored in its mass.
Energy can be stored in many different types of substances and systems.
A material can release energy in four types of reactions. These reactions are nuclear, chemical, electrochemical and electrical.
Energy density is generally expressed in two ways;
i. Volumetric energy density - how much energy a system contains in comparison to its volume; typically expressed in watt-hours per liter (Wh/L) or Megajoules per liter (MJ/L).
ii. Gravimetric energy density (Specific energy) - how much energy a system contains in comparison to its mass; typically expressed in watt-hours per kilogram (Wh/kg), or Megajoules per kilogram (MJ/kg).

## Slide 17: Energy densities of different fuels

## Slide 18: Combustion

## Slide 19: Combustion
Combustion is an exothermic chemical reaction, where a substance (which often refers to a fuel, carbonaceous material or hydrocarbon) reacts with oxygen to produce mainly heat along with other by-products (known as exhaust) such as carbon dioxide and water.
Combustion reaction initiated based on this three condition:
Combustible material – any substance containing carbon
Oxygen
Ignition temperature – for reaction to take place, the amount of energy supplied to the reactants has to be sufficient to overcome the activation energy of the reaction

## Slide 20: Combustion
Combustion is a rapid reaction between a substance and oxygen that releases heat and light energy.
A fuel is a substance that reacts with oxygen (combusts) to release useful energy.
Biomass is used as fuels because they burn easily and release a large amount of useful energy.

## Slide 21
Combustion of biomass has been widely used in the past to generate heat
At present, it is making a comeback in many industrial applications including generation of electricity,
Straightforward conversion of thermal energy into mechanical or electric power results in considerable losses
It is not possible to raise the ratio of thermal to mechanical power above 60%.
However, if the low temperature waste heat can be used productively, for instance for drying or heating purposes, much higher overall efficiencies can be obtained.

## Slide 22
Volatiles and Fixed Carbon
Volatiles: Flaming combustion
Fixed carbon: Glowing combustion

## Slide 23
Fuel | Volatile Matter | Fixed Carbon | Ash
Paddy Husk | 63.3 | 14.0 | 22.7
Bagasse | 74.0 | 19.3 | 6.7
Wood | 77 - 87 | 13 - 21 | 0.1 - 2.0
Lignite | 43.0 | 46.6 | 10.4
Anthracite Coal | 5.0 | 80 | 15

## Slide 24: Global distribution of biomass energy use in 2008 (Euromonitor International, 2009)

## Slide 25
Main reactions involved in a combustion reaction;

## Slide 26
A good combustion should fulfil this following rule:
Temperature – Must be sufficiently high to overcome the activation energy of reaction
Turbulent – Gives good mixing between fuel and air
Time – Must be long enough to reach complete combustion

## Slide 27: Combustion Controlling Factors
    Physical and chemical properties of the fuel;
    Fuel/air ratio;
    Temperature of the flame/envelope;
    Mode of fuel supply;
    Primary and secondary air supplies.

## Slide 28: Combustion technologies
Combustion technologies convert biomass fuels into several forms of useful energy for commercial or industrial uses: hot air, hot water, steam and electricity
A furnace is the simplest combustion technology:
biomass fuels burns in a combustion chamber
converting biomass into heat energy (hot gases contains 85 % of the fuel’s potential energy)
either direct or indirect use of heat exchanger to use the hot gases in the form of hot air or hot water
combustion of wood can be divided into four phases:
Drying: water inside the wood boils off
Degasification: gas content is freed from the wood
Gasification: the gases emitted mix with atmospheric air and burn at a high temperature
Combustion: the rest of the wood (mostly carbon) burns

## Slide 29: COMBUSTION
In simple terms, a steam turbine works by using a heat source heat water to extremely high temperatures until it is converted into steam.
As that steam flows past a turbine’s spinning blades, the steam expands and cools.
The potential energy of the steam is thus turned into kinetic energy in the rotating turbine’s blades. Because steam turbines generate rotary motion, they’re particularly suited for driving electrical generators for electrical power generation.
The turbines are connected to a generator with an axle, which in turn produces energy via a magnetic field that produces an electric current.

## Slide 30: Example of rice straw power generation

## Slide 31: Gasification

## Slide 32: Gasification
The gasification is a thermo-chemical process that converts any carbon-containing material into a combustible gas by supplying a restricted amount of oxygen.
In case of biomass feedstock, this gas is known as wood gas, producer gas or syngas, which composed primarily of carbon monoxide and hydrogen as fuels, together with small amount of methane.
It will also contain other compounds, such as sulfur and nitrogen oxides, depending on the chemical composition of the fuel.
Under typical gasification conditions, oxygen levels are restricted to less than 30% of that required for complete combustion.
The composition of the gasification gas is very dependent on the type of gasification process, gasification agent and the gasification temperature.
Based on the general composition and the typical applications, two main types of gasification gas can be distinguished as producer gas and syngas.

## Slide 33
Syngas has a calorific value, so it can be used as a fuel to generate electricity or steam or as
a basic chemical feedstock in the petrochemical and refining industries. The calorific value of
this syngas will depend upon the composition of the input waste to the gasifier.

## Slide 34: Gasification Agent:
    The oxidant for the gasification process can be either atmospheric air or pure oxygen.
    Air gasification of biomass produces a low calorific value (or Low Mega-Joule) gas, which contains about 50% nitrogen and can fuel engines and furnaces.
    Gasification of biomass with pure oxygen results in a medium calorific value (or Medium Mega-Joule) gas, free of nitrogen.
    These system also offer faster reaction rates than air gasification but has the disadvantage of additional capital costs associated with the oxygen plant.

## Slide 35: Gasification
Gasification process represented using different time zones in an updraft gasifier

## Slide 36
The moisture content of biomass is normally high (typically 30-60 wt% biomass).
Biomass feed is dried using the heat released from the downstream zones, commonly 100-200˚C.
Process does not involve interaction with air or oxygen, occur at 500˚C.
Producing pyrolysis oil or bio-oil.
There are two types of pyrolysis – fast and slow.
Primary pyrolysis occurs as soon as solid biomass comes into contact with the hot bed of gasifier before the main gasification reactions.

## Slide 37
Solid biomass and residual biomass undergo gasification in the gasifying medium such as air, oxygen and steam around 800-1000˚C.
Two main reaction occurs – exothermic partial oxidation and endothermic steam methane reforming.

## Slide 38
Gasification has two main reactions:
1. Heterogeneous reactions:
(partial oxidation reaction)
(water gas reaction)
(Boudouard reaction)
(methanation reaction)
2. Homogenous reactions:
(water gas shift reaction)
(steam methane reforming)
Boudouard reaction - Redox reaction of a chemical equilibrium mixture of carbon monoxide and carbon dioxide at a given temperature.

## Slide 39
Highly exothermic reaction step that supplies the majority of the heat to other reaction zones.
Reaction occurs at 1300˚C.
Oxidation reactions:
Char produced in the pyrolysis zone is around 20% of the original biomass by weight and passes through combustion and reduction zones.

## Slide 41: Comparison of gasifier technologies (a) fixed bed/ moving bed; (b) fluidized bed; (c)Entrained bed
Parameters:
Configuration
Principle of operation
Oxidation requirement (low/moderate/high)
Steam requirement (low/moderate/high)
Outlet gas temperature (low/moderate/high)
Feed size particles
Capacity
Cold gas efficiency
Advantages
Disadvantages

## Slide 42: Types of gasifier Fixed bed/ Moving bed gasifier
Updraft gasifier
Downdraft gasifier
Cross draft gasifier
Principle of operations
Fuel is fed from the top of the gasifier and flows downward.
Air/oxygen is supplied from the bottom (updraft) or a certain height from the bottom (downdraft/ crossdraft). Depending on the configuration, the syngas product leaves the gasifier either from the top (updraft), bottom (downdraft) or from the side (crossdraft).
The flow of fuel and air can be countercurrent (updraft) or cocurrent (downdraft and crossdraft).
Ash is collected at the bottom.

## Slide 43
Updraft gasifier
Downdraft gasifier
Crossdraft gasifier
Advantages
Need less oxidants
Disadvantages
High maintenance cost
Poor mixing and heat transfer
Produce considerable amount of tar and oil
Agglomeration

## Slide 44: Types of gasifier Fluidized bed
Bubbling fluidized bed gasifier
Circulating fluidized bed gasifier
All processes are taking place simultaneously throughout the reactor volume, although intensity may vary depending on the location

## Slide 45
Principle of operations:
Fuel particles float on a stream of air and sand at a velocity that is enough to keep suspension of the solid. Char particles leaving with the product gas at the top of the gasifier are recovered via a cyclone and recycled back to the gasifier. The operating temperature is kept below the ash fusion temperature.
Advantages:
Uniform temperature distribution
Good mixing
Lower risk of agglomeration
Produce less tar and oil
Disadvantages:
Extensive solid (char) recycling

## Slide 46: Types of gasifier Entrained bed
Principle of operation:
Fuel particles and oxidant are gasified under high temperature (higher than the slag fusion temperature) in a very short residence time to achieve high carbon conversion. Oxygen is generally used as the oxidant.
Advantages:
All types of fuel rank can be gasified
Elimination of tar
Disadvantages:
Require a large amount of oxidant
High temperature slagging operation
Require very fine fuel particles as feedstock
Entrained bed gasifier

## Slide 47: What is the type of this gasifier?
Downdraft gasifier

## Slide 48: Factors Affecting Rate of Gasification
  Apart from the basic technology and design aspects of gasifiers, the rate of gasification is affected by several factors including the following.
    The size of the feeding material particles (small; large) and its distribution
    The shape of the particulates (powdery  lump)
    The structure of the material (porous  non-porous)
    Environment (Reactive: Air/Oxygen  Inert: Nitrogen/Argon)
    Flow of medium (Static  Continuous)
    Heating rate (Slow  Fast)
    Temperature (Low: < 500 C  High: > 500 C)
    Ash (Catalytic  Non-catalytic)

## Slide 49: Design consideration of gasifier
Specification | Options
Pressure Atmospheric Pressurized | Suitable and more economical for small-scale application. However, high cost would be incurred in the downstream processes, such as syngas cleaning and conditioning, synthesis processes and electricity generation, which demand higher pressure. Thus, higher compression power is required for the downstream processes. High pressure is favorable for most of the downstream processes. This would result in a more economic design, since less compression power is needed. However, extra caution has to be taken for the safety of the gasifier.
Gasifying medium Air Oxygen | Air is cheaper than oxygen. However, air has a significant amount of nitrogen (∼79 mol%), which has a dilution effect on the product gas stream. This would lower the heating value of the product gas. The dilution effect of nitrogen leads to inefficiency in CO2 removal and also the downstream production. Furthermore, larger unit operations are needed for the entire system. Highly pure oxygen is expensive compared to air since it requires high capital investment and operating cost for an air separation unit or an oxygen plant. However, it prevents product gas from dilution and retains the heating value of product gas. In addition, the unit operations are smaller for the whole system.
Syngas Cooling Quench Heat recovery | Heat is not recovered and is downgraded to process heat. A lower capital cost is needed and thus it is suitable for the low value feedstock. If water gas shift is used downstream, then the quench design provides enough water for the reaction. Allows heat recovery and produces steam, leading to a more energy efficient system.

## Slide 50
Use of gasification for generation of fuels, chemicals and power

## Slide 51: Gasifier end-uses
Syngas or producer gas can be burned to create heat, steam, or electricity.
It can be converted to methane and fed into a natural gas distribution system.
Syngas can also be converted to methanol, ethanol, and other chemicals or liquid fuels.
Methanol produced through gasification can be further refined into biodiesel with addition of vegetable oils or animal fats
Use of gasification for generation of fuels, chemicals and power

## Slide 52: Advantages of Biomass Gasification
CONVENIENT - Produces a more convenient easily controllable form of cleaner fuel for both thermal energy and electricity generation, and provides a mean to reduce or remove conventional fossil fuels.
FLEXIBLE - Gasification gives biomass the flexibility to fuel a wide range of electricity generation systems: gas turbines, fuel cells, and reciprocating engines.
VARIETY - A wide variety of biomass materials can be gasified, many of which would be difficult to burn otherwise.
CLEANER - Gasification has the potential of reducing emission of pollutants and greenhouse gases per unit energy output.
EFFICIENT - Projected process efficiencies are higher than the direct combustion systems and comparable with fossil systems.

## Slide 53: Design of gasifier
1. Feed stock consumption rate;
2. Dimension of reactor shell;
3. Height of the reactor;

## Slide 54: Pyrolysis

## Slide 55
Pyrolysis
( Greek-derived: pyro "fire" and lysis "separating“ )
Thermal decomposition process, which occurs in the absence of or little oxygen environment.
Involves the simultaneous change of chemical composition and physical phase and is irreversible.
Bio-Oil is the main product of pyrolysis.

## Slide 56
A. Demirbas, G. Arin. Energy Sources Part A, 24 (2002), p. 471

## Slide 58: Fast Pyrolysis
Feed preparation
Biomass needs to be ground into fine particles before the pyrolysis reaction. The reasons are:
To achieve high surface area per unit volume for reaction.
To avoid build-up of char on the surface of biomass; char hinders heat transfer to the centre of particles.
Quenching (rapid cooling) of the pyrolysis vapours to give the bio-oil product.

## Slide 59: Pyrolysis product
Depending on the thermal environment and the final temperature, pyrolysis will yield: Bio-oil, biochar, gaseous

## Slide 60: Production of bio-oil

## Slide 61
Physical appearance and characteristics
Dark brown in color, has smokey smell.
Immiscible with petroleum, cannot be introduced directly into conventional refinery.
Viscosity 40 to 100 cP at 40˚C with 25% water
Chemical properties
High proportions of oxygen (45-50%) and water (15-35%)
Chemically unstable due to presence of reactive components – aldehydes
Highly acidic (pH 2-3) due to presence of carboxylic acids – lead to corrosion in equipment.
Applications
Electricity generation via turbines, engines or boilers.
Fuel for transportation and chemical production.
Advantages
Cleaner, with negligible amount of sulfur, nitrogen, ash and other impurities.
Has higher bulk energy density than solid biomass.
Inert and nontoxic properties.
Separate into heavy organic fraction that sinks.

## Slide 62: Challenges for large scale production of bio-oil
Expensive – the cost of bio-oil is 10-100% higher than fossil fuel
Availability – limited supplies for testing
Quality – specification of bio-oil has not been standardized and has inconsistent quality
Compatibility – incompatible with fossil fuels
Familiarization – many users are not familiar with bio-oil
Environmental health and safety issues

## Slide 63: Biochar
Combustion and decomposition of woody biomass and agricultural residues results in the emission of a large amount of CO2. Biochar can store this CO2 in the soil leading to reduction in GHGs emission and enhancement of soil fertility.
Replacement for other biomass energy systems

## Slide 64: Type of pyrolysis reactor
Bubbling fluidized bed pyrolysis reactor
Circulating fluidized bed pyrolysis reactor
Ablasive pyrolysis reactor
Auger/ screw pyrolysis reactor
Rotating cone pyrolysis reactor
Vacuum pyrolysis reactor

## Slide 65: Bubbling fluidized bed pyrolysis reactor
Principle of operation
A stream of gas (normally recycled pyrolysis gas) is used to fluidize biomass particles together with hot sand. Heat is supplied to the bed using either the process heat through the preheated fluidized gas (adiabatic) or sand that is indirectly heated by fired tubes. The former method normally allows a smaller throughput for the reactor design while the latter gives a better performance.
Advantages
-Well established with long operating history
-High heat transfer rate
-Good temperature control
-Simple design
Disadvantages
-Normally small throughput (heat supply is major consideration for scaling up the reactor)
-Feed has to be carefully sized (narrow particle size distribution).

## Slide 66: Circulating fluidized bed pyrolysis reactor
Principle of operation
The principle is similar to fluidized bed except that it involves solid transport between two vessels, i.e., pyrolyzer and combustor. Sand is transported together with char to combustor and recirculated back to pyrolyzer.
Advantages
-High heat transfer rate
-Large throughput is possible
-Good temperature control
Disadvantages
-High energy need for circulating sand
-Wear problem in the reactor
-High gas velocity leading to higher char abrasion and hence higher char content
-Ash build-up in the circulating solid cousing further cracking and thus reducing the bio-oil yield

## Slide 67: Ablasive pyrolysis reactor
Principle of operation
Biomass particle is melted under pressure on the hot surface of reactor (similar concept to melting a slice of butter over a frying pan).
Advantages
-Large feed particles can be used
Disadvantages
-Wear problem in the solid recycle loop.
-Scale up is difficult
-High gas velocity causing erosion

## Slide 68: Auger screw pyrolysis reactor
Principle of operation
Sand and biomass are fed to screw and transported to reactor. Mixing and heating are carried out using rotational screw and transported to the reactor. The concept originated from Lurgi coal gasifier.
Advantages
-Low operating temperature
Disadvantages
-Heat transfer at large scale can be a problem

## Slide 69: Rotating Cone Pyrolysis Reactor
Principle of operation
Centrifugal force drives the biomass and sand from the bottom of the cone to the top. High speed rotation provides good mixing and heat transfer. Vapor is directed to a condenser. Sand is reheated in a combustor and sent back to the base of the cone.
Advantages
-Carrier gas is not needed, recovery of bio-oil product is easier.
-Less aggressive transport dynamics of sand and biomass, hence wear problems can be minimized.
Disadvantages
-Integration is complex
-Scale up is uncertain

## Slide 70: Vacuum pyrolysis reactor
Principle of operation
The boiling point of biomass is lowered due to reduced pressure condition (∼0.15 bar). After decomposition through heating, the small fragment is immediately removed using a vacuum pump and recovered as liquid product through condensation. This results in a shorter vapor residence time for reaction and, hence, secondary reactions can be minimized.
Advantages
-Produces clean oil with little char -Large particles size of biomass can be used -Carrier gas is not needed, minimizing aerosol formation
Disadvantages
-Slow pyrolysis process due to poor heat and mass transfer rate -Low bio-oil yield -Generates significant amount of water -High cost for maintenance `