## Slide 1: EKC 464 BIOREFINERY ENGINEERING
Nur Ayshah Rosli, PhD
Room No: 2.22
Ext: 6487

## Slide 2: MEMBRANE SEPARATION
Microfiltration, Ultrafiltration and Diafiltration Nanofiltration Membrane Pervaporation Membrane Distillation

## Slide 3
Membrane separation is a technology which selectively separates (fractionates) materials via pores and/or minute gaps in the molecular arrangement of a continuous structure. Membrane separations are classified by pore size and by the separation driving force.

## Slide 4
A schematic of a process for the fractionation of substances in biorefinery process streams
Membrane processes are expected to be key components in biorefineries because of their low energy requirement and low chemical consumption.

## Slide 5
Solids that could block the flow channels of membrane modules in the subsequent stages are removed, for example, by filtration or centrifugation (F&C) of the process stream.
Suspended solids and colloidal matter (e.g. extractives) are separated by microfiltration (MF).
Macromolecules, for example hemicelluloses and protein, are concentrated by ultrafiltration (UF).
Monosaccharides, multivalent inorganic ions and low-molar-mass lignin are concentrated by nanofiltration (NF) and salts are removed by reverse osmosis (RO).

## Slide 7: Membrane separation

## Slide 8: Separation triangle

## Slide 9
Industrial membrane processes may be classified according to the size range of materials which they are to separate and the driving force used in separation. There is always a degree of arbitrariness about such classifications, and the distinctions which are typically drawn are shown in Table below:

## Slide 10: Membrane material
Membranes may be composed of natural (e.g modified natural cellulose polymers ) or synthetic polymers (plastic materials) or inorganic ceramic materials
good film formers
manage high permeate flows
high selectivity
good chemical and bacteriological resistance
resistant to detergents and disinfectants
inexpensive

## Slide 11: Membrane modules
A membrane module is a complete unit composed of the membranes, a housing, feed inlet, concentrate outlet, and permeate outlet.
Membrane module configurations:
tubular modules
plate-and-frame modules
spiral-wound modules
hollow-fibre modules
rotating and vibrating modules.
Different in term of:
Price
Footprint
risk of blockage of the feed flow channel.

## Slide 12
The choice of the most suitable membrane module type for a particular membrane separation must balance a number of factors:

## Slide 13
The types of modules generally used in some of the major membrane processes

## Slide 14: Design and operation of membrane plants
Pumps - Follow the recommendations of the membrane manufacturer.
Construction materials - good quality, preferably stainless steel for all parts and devices that come into contact with liquids. Rust will not only cause fouling, but can also increase the osmotic pressure.
Dead spaces - must be avoided, source of bacterial growth, fouling
Rinse and clean - Never leave the process solution in a membrane plant
Start-up and shut-down - The pressure should be increased gradually at start-up in order to avoid high initial concentrations at the membrane surface when the flow resistance of the clean membrane is low. Gradual changing of the temperature when rinsing the system during shut-down is recommended, in order to prevent the precipitation of solutes.

## Slide 15: Economic considerations
Separation accounts for 60 to 80% of the process cost in most mature chemical processes
Design and optimization of the separation process are therefore vital in order to reduce costs.
Minimizing the cost of membrane plants is generally a trade-off between high flux and a low energy requirement. Flux usually increases with increasing pressure and cross-flow velocity, but so does the energy required.
In most cases, the capital cost is the largest cost in a membrane plant. The main operating costs are: for electricity, replacement of membranes and cleaning; maintenance and labor cost.

## Slide 16: Process Design
Flux during concentration - The flux decreases as volume reduction (VR) increases
The average flux during batch concentration:
where a, b, c and d are polynomial coefficients.

## Slide 17
Retention – A membrane that retains all solutes has a retention of 100%, and the retention is 0 if no solutes are retained.
The retention is defined as:
where Cp and Cr are the concentrations in the permeate and in the retentate.
If the retention is constant during concentration, the correlation between the retentate concentration and VR in a batch process follows the relationship
where C 0 is the initial concentration.
The retention of multidisperse compounds commonly increases during concentration.

## Slide 18
Recovery and purity
Recovery is the fraction of a component in the feed that is collected as a useful product. If the retention is constant during concentration and the retentate is the product, recovery is given by:
where mr and m0 are the amounts of substance in the retentate and feed.
If R < 100%, part of the product is lost with the permeate during concentration, which reduces the recovery. If the retention is zero, the concentration in the permeate is similar to that in the retentate, and the amount removed depends only on the VR

## Slide 19
Purity of the product depends on the concentration of all compounds in the product stream.
The purity of the product in the retentate is:
where Cr and ƩCi are the concentrations of the product and of all compounds in the retentate.

## Slide 20: Operating parameters
• the transmembrane pressure (TMP); • the cross-flow velocity; • the temperature; and • the pH.

## Slide 21: Pressure
The pressure in a membrane plant is measured at the inlet, pin, and outlet, pout, of the membrane module and on the permeate side, pp
The transmembrane pressure, is the driving force in UF and MF. The TMP used in the following Equation is generally the average pressure difference across the membrane:

## Slide 22
The TMP is usually regulated by the retentate valve.
However, when using ceramic membranes the TMP is often regulated by a valve on the permeate side of the module.
If there is no permeate valve, the permeate pressure equals atmospheric pressure.

## Slide 23
The frictional pressure drop is the pressure difference between the inlet and outlet of the module.
The pressure drop is often negligible in small bench-scale membrane modules but can be significant in full-scale modules.
If the inlet pressure is high, as during UF, the difference between the pressure at the inlet and the outlet is usually small enough to be considered negligible.

## Slide 24
Cross-flow velocity is employed to reduce concentration polarization and increase mass transfer
In the film theory, the fluid flow in the boundary layer adjacent to the membrane surface is assumed to be laminar, whereas the fluid flow outside this layer is turbulent with complete mixing of the solute.
At steady state, the convective solute transport in the boundary layer is equal to the permeate flow, and the diffusive back transport of solute into the bulk solution.

## Slide 25
The correlation between flux and concentration at the membrane surface given by the film theory model is:
where k = D/δ is the mass transfer coefficient and Cm, Cb and Cp are the concentrations at the membrane surface, in the bulk solution and in the permeate. D is the diffusion coefficient and δ is the thickness of the boundary layer.

## Slide 26
In order to increase the flux, the mass transfer coefficient is normally increased by decreasing the boundary layer thickness.
In most modules the shear rate is enhanced by increasing the cross-flow velocity.
The mass transfer coefficient is also influenced by the viscosity, and hence by the concentration of the feed solution.

## Slide 27: Temperature
Increasing the feed solution temperature leads to three flux enhancing effects:
The viscosity of the permeate decreases which results in a higher flux
The lower viscosity of the solution on the feed side of the membrane improves the mass transfer coefficient
The lower bulk solution viscosity increases the Reynolds number, and hence, lowers the frictional pressure drop, which also has a positive effect on flux.

## Slide 28: Concentration
Membrane processes are limited in the degree of concentration of the feed solution.
No membrane process can concentrate solutes to dryness.
In RO and NF processes, it is frequently the osmotic pressure of the concentrated solute that limits the process.
In MF and UF processes, it is rarely the osmotic pressure, but rather the low mass transfer rate of the high-molar-mass substances retained by these membranes, and the high viscosity, that make pumping of the retentate difficult, limiting the final concentration.
Flux decreases as the concentration increases
The increased concentration at the membrane may decrease retention and increase fouling.

## Slide 29: Diafiltration
In diafiltration (DF) the product is purified by removing permeable solutes by dilution with water.
Diafiltration is used to purify the product when the purity is not sufficient after UF.
In discontinuous DF, freely permeable solutes are removed from the retentate by volume reduction using UF (preconcentration), followed by dilution with a solvent (usually water) and concentration of the diluted solution by UF (final concentration).
Dilution and UF are repeated until the desired purity is achieved.

## Slide 30: Fouling and cleaning
There are three main fouling mechanisms: cake layer formation, pore blocking and adsorption
Cake layer formation and pore blocking can occur if the solute molecules are large enough to be retained by the membrane.
If, on the other hand, the solute molecules are small enough to enter the pores they may be adsorbed onto the pore walls of the membrane.
The adsorbed molecules can then reduce the effective pore diameter resulting in an increase in the membrane resistance.

## Slide 31
Cake formation is reduced by:
operating below the critical flux
using backpulsing
pore blocking by using membranes with smaller pores and adsorption is commonly reduced by using hydrophilic membranes
adjusting the pH

## Slide 32: Pretreatment
The fouling tendency of a solution may be reduced by suitable pretreatment of the solution, be it mechanical, thermal or chemical.
Common modifications to the feed solution include:
adjustment of the pH
The removal of fibres and particles.
As a rule of thumb, the maximum particle size in the feed should be one-tenth of the smallest dimension of the feed channel

## Slide 33: Cleaning
Cleaning cycle generally includes the following stages:
• removal of product from the system;
• rinsing the system with water or permeate;
• cleaning in one or several steps;
• rinsing the system with water; and
• disinfection of the system (if required)
Cleaning process for each application is different depending on temperature, time, concentration and type of cleaning agent.

## Slide 34: Nanofiltration examples in biorefineries
Recovery and purification of monomeric acids - Separation of lactic acid from cheese whey fermentation broth
Fermentation products are typically in the nanofiltration size range.
Lactic acid can also be produced from lactose by fermentation of lactose-rich raw materials like cheese whey.
Ultrafiltration combined with diafiltration is used to concentrate and purify whey proteins from lactose, salt, and other components in the whey.
Nanofiltration retained about 97% of the lactose and 40% of the lactic acid from the fermentation broth.
The permeated lactic acid was concentrated at 55 bar pressure using reverse–osmosis (RO) membrane.

## Slide 35
Recovery and purification of monomeric acids - Separation of lactic acid and amino acids in fermentation plants
A demonstration plant was constructed in Austria to produce lactic acid and various amino acids from pressed silage juice.
After sedimentation of the juice the first step is ultrafiltration, in which disturbing macromolecules and proteins are separated from the product permeate stream.
The UF permeate is then treated by nanofiltration to produce phases enriched in amino acids (concentrate) and lactic acids (permeate).

## Slide 36
Biorefineries connected to pulping processes
Separation of sugars from acids or other impurities can be done by NF and a simultaneous purification and concentration is possible to achieve.
Fractionation of different organic acids might also be a future application for nanofiltration membranes in biorefineries.
Purification of monosaccharides from lignin can partly be made by ultrafiltration or NF.

## Slide 38: Membrane pervaporation
Pervaporation (PV) is a separation process for liquid mixtures by means of a nonporous membrane.
The membrane acts as a barrier between a liquid phase (feed) and a vapour phase (permeate).
Pervaporation is a membrane process technology combining membrane permeation and evaporation for molecular-scale liquid separation.

## Slide 39: Drawbacks of the Existing Method (Distillation)
Distillation is a conventional liquid mixture separation technology based on their boiling points.
Disadvantages of distillation - Difficult to separate liquids mixtures which the components have similar boiling point (azeotropes).
Advance in technology - Pervaporation can be used for breaking azeotropes.

## Slide 41: Applications of pervaporation
the dehydration of organic solutions
the removal or recovery of small amounts of organic volatiles from mixtures
the separation of organic-organic mixtures

## Slide 42: Challenge for industrialization of pervaporation
Current permeation flux is too low to be economical.
The high costs of membrane production and module fabrication
Problems associated with membrane reliability and resistance to harsh environments

## Slide 43: Pervaporation mechanism
Sorption of the permeate from the feed liquid to the membrane
Diffusion of the permeate through the membrane
Desorption of the permeate to the vapor phase on the downstream side of the membrane
Permeation rate and selectivity are governed by the solubility and diffusivity of the feed components permeating across the membrane.

## Slide 44: Pervaporation performance parameter
Selectivity – what goes through and what gets rejected
Flux – denote the amount of output (measured in relation to membrane area, thickness and time)
Membrane thickness – refer to dry thickness
Temperature – feed temperature
Kinetic diameter – diameter of pore needed to let specific molecule pass

## Slide 45: Design principles of the pervaporation membrane
Adopt two strategies in biorefinery:
Molecular design of membrane materials with desired physicochemical properties (inherent solubility, diffusivity, and selectivity
Design a desired membrane morphology with ultrathin and defect-free dense selective layer

## Slide 46: Example of membrane selection
Application – bioethanol dehydration
Polymer - PVA, chitosan, sodium alginate, polyimide, polyacrylic acid
Similar features: plentiful polar functional groups, excellent hydrophilicity, also exhibit high-abrasion resistance, elongation, tensile strength, and flexibility (upon modification)

## Slide 47
Separation performance of various NaAlg-based membranes for ethanol dehydration

## Slide 48
Application – bioethanol dehydration
Inorganic pervaporation membranes – silica, zeolite
Properties - unique pore structure, adsorption properties, as well as good mechanical, chemical resistance and thermal stabilities
Organic–inorganic hybrid also shown a potential in alcohol-water separation. E.g: Cross-linked PVA membrane on hollow fibre alumina support, Ceramic-supported P84 polyimide membranes

## Slide 49
Separation performance of inorganic membranes for ethanol dehydration

## Slide 50: Membrane morphology
Different membrane morphologies:
(a) Dense film membrane, (b) Asymmetric membrane, (c) Composite membrane, (d) Single-layer hollow fiber membrane, and (e) Dual-layer hollow fiber membrane
Hollow membrane:
(i) a larger membrane area per unit membrane module
volume, resulting in a higher permeation flow per unit volume;
(ii) self-supporting structure, allowing the membrane to be a self-contained vacuum channel, where the feed can be supplied from the shell side while vacuum is applied on the lumen side; and
(iii) good flexibility and ease of handling during module
fabrication and system operation.

## Slide 51: Pervaporation in the current integrated biorefinery system Process designs of butanol production
conventional process
integrated process with product separation inside the fermenter
integrated process with product separation outside the fermenter.

## Slide 52: In the production of high concentrated ethanol from untreated sugar cane, integration of ultrafiltration and pervaporation processes are employed downstream of the bioreactor.
Importance of integration - Energy-efficient process for achieving high-purity products and increasing overall production.
The main advantages of an integrated ultrafiltration-pervaporation system in the fermenter are:
(i) to recycle the cells back to the fermenter
(ii) to remove the ethanol itself, which acts as an inhibitor at high concentrations;
(iii) to prevent fouling in the pervaporation membrane.

## Slide 53: Illustration of hybrid system for biorefinery via synergetic recovery-dehydration pervaporation processes.
By coupling pervaporation units with a distillation process:
the number of trays in the distillation column is reduced, thereby reducing the complexity of the column design.
In addition, the hybrid process lowers energy (thermal) consumption and brings down the operating cost, which can compensate for the high previous investment cost of distillation columns

## Slide 54: Membrane Distillation

## Slide 55: Transport mechanism
Separation process where a micro-porous hydrophobic membrane separates two aqueous solutions at different temperatures.
The hydrophobicity of the membrane prevents mass transfer of the liquid, whereby a gas-liquid interface is created.
The temperature gradient on the membrane results in a vapour pressure difference, whereby volatile components in the supply mix evaporate through the pores (10 nm – 1 µm) and, via diffusion and/or convection of the compartment with high vapour pressure, are transported to the compartment with low vapour pressure where they are condensated in the cold liquid/vapour phase.

## Slide 56: Characteristics of MD
The membrane must be porous and hydrophobic (that is, the membrane must not be wetted by the process liquids).
The membrane does not alter the vapour-liquid equilibrium of the different components in the process liquids.
The driving force for each component is a partial pressure gradient in the vapour phase.
At least one side of the membrane must be in direct contact with the process liquids.
No capillary condensation must take place inside the pores of the membrane.

## Slide 57: Advantages of MD
High quality of distillate. Theoretically, 100% of ions, macromolecules, colloids, cells, and other non-volatile components are rejected.
Lower operating temperatures.
Low-grade waste and alternative energy sources such as solar and geothermal energy may be used.
Lower operating pressures.
Fewer demands about membrane mechanical properties.
Chemical interaction between membrane and process liquids is very reduced. The membrane acts merely as a support for the vapour liquid interface.

## Slide 58: Configuration types of MD
direct-contact membrane distillation (DCMD)
air gap membrane distillation (AGMD)
sweeping gas membrane distillation (SGMD)
vacuum membrane distillation (VMD)

## Slide 60: Application of MD in biorefineries
MD-bioreactor hybrid - separation of ethanol and the other inhibitory compounds from fermentation broths
Advantages:
increase in ethanol production - maintain a low ethanol concentration in the broth, thereby alleviating the problem of product inhibition.
more complete fermentation of sugars
lowering the osmotic pressure in the fermentation broth
decreasing glycerol synthesis level
increasing yeast cells’ number and viability.

## Slide 61: Challenges
Low permeate flux
Problem of developing highly hydrophobic, stable, microporous membranes
Control the fouling problems

## Slide 62: SOLID-LIQUID SEPARATION

## Slide 63: Principles solid-liquid extractions
Solid–liquid extraction allows soluble components (solute) to be removed from solids using a solvent.
The SLE process can be considered in three stages:
1. Diffusion of the solvent through the pores of solid.
2. Dissolution of the solute in the solvent to form miscellar, as the solvent enters the solid.
3. Transfer of the miscella back to the bulk solvent.

## Slide 64: Extraction mode
Percolation
the solvent flows through solid fixture.
In batch process, the solid is a fixed bed, whereas in continuous process, the solid is retained on a perforated conveyor or basket.
This method is very popular for extraction of large amounts of solids

## Slide 65: Extraction mode
Dispersed solids
the solid is retained in the solvent throughout the extraction process.
The solid is usually pretreated, i.e. pulverized and/or dried, before being fed into the extractor.
This method produces a higher yield compared to the percolation method but the operating cost is higher.
Two method in this category: immersion (immerse the solid particles in the stirred solvent) and maceration (soak the solid in the solvent without agitation)

## Slide 66
Solid-Liquid Extraction
i. Solvent extraction
ii. High pressure extraction
iii. Ultrasonic-assisted extraction
iv. Microwave-assisted extraction
v. Heat reflux extraction

## Slide 67: Solvent extraction
A compatible solvent is added to a solid in order to extract the solute from the solids.
The exhausted solid (solid discharge) will later be separated from the miscella (mixture of solvent and solute) by filtration or gravity.
The extract in the miscella will be purified using evaporation, drying, or distillation.

## Slide 68: High pressure extraction
Alternative technique for substances that are sensitive to high-temperature processing
up to 1000 MPa
High pressure can cause some structural changes on the solids, thus improving the mass transfer rate, and subsequently providing faster and more effective extraction.
supercritical fluid extraction (SFE)

## Slide 69: Ultrasonic-assisted extraction
Uses ultrasonic waves (18–20 kHz) to aid the extraction process by disrupting the solid structure
The structural change is induced by the cavitation effects from the ultrasonic irradiation.
pretreatment and extraction of plant materials

## Slide 70: Microwave-assisted extraction
Microwave-assisted extraction (MAE) has many advantages over other extraction methods, such as low solvent usage and shorter extraction time.

## Slide 71: Heat reflux extraction
Reflux extraction is done by boiling the material in the solvent, and a chilled surface is used to condense the rising solvent vapors.
The solvent vapors are returned to a liquid state in the container and continue to be boiled without the solvent boiling away.
Then, the extract continues to concentrate in the solvent until it is reduced to essence later.

## Slide 72: Current technology for SLE
Current conventional – batch mode, 100-200˚C
The main constraint of these conventional methods is the long processing time and require large volumetric vessel to cater for a larger operation.
Efficient leaching will require a multistage operation to provide a better product yield.
For large-scale operations, continuous processes are favored. The design of equipment for continuous process is relatively compact and small
working capacity of between 100 to 17 000 tonnes per day

## Slide 73: SLE process for biorefineries
Pretreatment of raw materials
Extraction
Solute separation
Solvent recovery

## Slide 74: Pretreatment of raw materials
Solid–liquid extraction in biorefinery deals with agricultural resources like corn, corn stover, straw, and others.
A plant cell is protected by a cell wall that supports its rigid structure. The vacuole, nucleus and microbodies are present in the cytoplasmic area enclosed by a cell membrane.
The solute is available inside the body of solid, on the surface of the solid, inside pores, or scattered within the plant structure, i.e. leaf, stem, flower and root.
The extent of cell rupture and also the cell’s complex structures, determine the solute’s diffusivity.

## Slide 75: Cont..
Typically, cell walls can be disrupted by mechanical, chemical, physical, thermal or biological methods
Mechanical methods - bead mill and homogenizer, ultrasound
Enzymatic – pectin, cellulose; may cause higher for enxyme removal
Size reduction can be achieved by crushing, grinding, flaking, milling, or cutting into small pieces.
Shape modifications, like decortications, rolling, screw pressing, extruding, and pelletizing
It is vital that the solid is of a suitable size (surface area per unit volume) to increase the interfacial area for facilitating solute accessibility to the solvent.

## Slide 76: Cont..
But!
Fine sizes can create undesirable dense solid packing and may contribute to the blockage of the interstices of larger particles.
Causes difficulties in later separation.

## Slide 77: Solid–liquid extraction
Leaching process – by selective solvent (have affinity to solute of interest).
Hexane is known to be the most widely selected solvent to be used for extracting non-polar solutes like oil.
The extraction process must be manipulated as efficiently as possible to get a high yield and high purity of desired components with minimal carry-over of undesired byproducts or impurities.
High selectivity and low reactivity.
The solvents should also possess low specific heat and low latent heat of vaporization to assist separation and recovery after the extraction process.

## Slide 78
Hexane is used for the extraction of non-polar solute due to low cost and toxicity, good extraction efficiency, and ease of operation compared to other non-polar solvents such as petroleum ether, benzene, chloroform, isopropanol, and toluene.
However, the concern with hexane is that it is flammable, explosive, and toxic.
Other commonly used solvents for plant extraction are water, alcohols, glycol, acetates, and compressed/supercritical gas.

## Slide 79: Solubility in SLE
Plays important role
Affected by operating temperature
High temperature, high solubility of solute in solvent. Increasing diffusion coefficient and extraction rate – increased yield.
Yield increase when extraction temperature near to boiling point of solvent.

## Slide 80
WHAT HAPPEN IF THE TEMPERATURE TOO HIGH?
solvent losses by evaporation
extraction of undesirable constituents
damage to sensitive equipment
Enzyme attack
product damage.

## Slide 81: Solvent-to-solid ratio
Sufficient amount of solvent should be available for dissolving the solute and transferring it to the exterior of the solid matrix
Excessive use of solvents is commonly unfavorable.
agitation of fluids can promote effective use of all the interfacial surface of solid, eddy diffusion, mass transfer of solute from surface of solid to bulk of solutions.

## Slide 82
It takes 10,000 roses to fill a single 5ml bottle (about the size of your thumb)!

## Slide 83: Operational setup for SLE
Efficiency of SLE depends on
Equipment selection
Mode of operation (batch or continuous)
Solid handling (fixed bed, percolation, full immersion, intermittent drainage or dispersed/moving contact)
Arrangement of operation (single stage or multistage)
Dimension of extractor unit

## Slide 84: Industrial extractors
Production of edible oil (vegetable, soybean, sunflower)
Essential oils
Extracts for perfumes, health supplements, Ayurvedic and traditional Chinese medication regiments
Special chemicals (phytosterols, polyphenols)

## Slide 85: Future for SLE
To improve SLE processes by making them on a larger scale, with a shorter processing time and higher extraction yield.
Develop suitable model for scale up

## Slide 86: HYBRID/INTEGRATED REACTION-SEPARATION SYSTEMS—PROCESS INTENSIFICATION
Membrane Bioreactors for Biofuel Production Extraction-Fermentation Hybrid (Extractive Fermentation) Reactive Distillation for the Biorefinery

## Slide 87
The energy cost for the recovery and purification of a fermentation product is high, usually ranging from around 20% to 50% of the final product cost.
The recovery cost usually increases inversely proportional to the product concentration in the fermentation broth.
It is therefore important to have the fermentation product produced at a sufficiently high concentration before final recovery and purification.

## Slide 88
Opportunities for integrating membrane separations in the biofuel production in accordance with
membrane cut off category and biofuel calorific value

## Slide 89: Membrane Bioreactors for Biofuel Production
Bioreactor with recirculation in an external side stream cross-flow membrane module
Submerged membrane bioreactor with
internal membrane module

## Slide 90: Bioethanol production

## Slide 91: Advantages of membrane bioreactors Bioethanol production
Achieve high cell concentration retention to improve productivities, with simultaneous removal of ethanol and by-products to avoid inhibition.
Enrich fermentation product to high grade ethanol >98%, using low energy intensive processes.
Reduce costs with hydrolytic enzymes in saccharification stage and remove solids and inhibitory compounds from the stream fed to the fermentation.

## Slide 92
Upstream saccharification stage: Retention of hydrolytic enzymes and sugar permeation
Saccharification of starch and lignocellulosic compounds into sugar monomers is required prior to their fermentation into ethanol.
But chemical hydrolysis enzyme is toxic to microorganism.
Retention of enzyme with membranes as alternative
This alternative would allow:
recycling enzymes, bringing down operation costs
maintaining a constant product flux, with continuously permeation of cellobiose and glucose formed, which are strong inhibitors of the hydrolytic enzymes
Retaining suspended solids and cellulosic compounds contributing to a fully substrate hydrolysis and a cleaner fermentation feeding stream, with reduced suspended solids and macromolecules toxic to microorganisms used in ethanol fermentation.

## Slide 93: Biodiesel production

## Slide 94
Ultrafiltration membrane reactor operate based on reversed micellar medium because the cutinase is confined in the reaction medium, while allowing the enzyme re-use and the removal of the products.
Membrane: tubular ceramic membrane, made on Zirconium layer over a porous carbon support and it is highly resistant to pressure, temperature, pH, and organic solvents.

## Slide 95: Biogas production
Biogas is usually produced by anaerobic digestion of different wastes.

## Slide 96
Bioreactors with recirculation into external cross flow membrane module for biogas production

## Slide 97
The main challenge for anaerobic membrane bioreactors has been the fouling of membranes.
Membrane fouling is the result of adsorption of organic matter, precipitation of inorganic matter, and adhesion of microbial cells to the membrane surface.
Submerged membrane bioreactor technology had been applied as a strategy to control the development of fouling by cake layer formation.

## Slide 98
Submerged internal membrane bioreactors system for biogas production

## Slide 99: Applications of membrane bioreactors
Biobutanol recovery from fermentation broth
Algae harvesting for biodiesel
Purification of biohydrogen

## Slide 100: Extraction-Fermentation Hybrid
Extractive ABE fermentation for enhanced butanol production
ABE stands for acetone-butanol-ethanol
Butanol is the most desired product from ABE fermentation and yet the most toxic product to the culture.
Severe butanol inhibition exists in ABE fermentation, which results in low final butanol concentration, low yield, and low productivity

## Slide 101
in situ recovery of butanol is crucial
Simultaneous butanol recovery can relieve the product inhibition and leads to a more complete conversion of the carbon source.
Integration with fermenter including liquid–liquid extraction, adsorption, pervaporation and gas stripping.

## Slide 103: Extractive fermentation for organic acids production
Extractive fermentation selectively removing the desirable product also significantly increased the product yield due to reduced byproducts formation.
However, solvent toxicity and nutrients removal from the fermentation media by solvent extraction or adsorption could significantly lower cell productivity and thus reduce reactor productivity.

## Slide 105: Reactive Distillation
Reactive distillation is a unit operation in which chemical reaction and distillation occur simultaneously in a single piece of equipment.

## Slide 106: Limitation
Reactions of interest must occur at temperatures and pressures that are compatible with the desired distillation.
Cannot be applied to gas–liquid reactions that require very high temperature and pressure.
Difficult to implement for very slow reactions; the extended catalyst contact times required result in large column sizes that are expensive to build and challenging to operate.
Maintaining proper chemical gradients to drive reactions forward can be challenging because of mass transfer or volatility issues
Need long catalyst life
complexity of simultaneous reaction and separation – challenging to design
Additional cost

## Slide 107: Flow diagram for biodiesel synthesis via reactive distillation

## Slide 108: Process concept for ethyl lactate production via reactive distillation

## Slide 109: Reactive distillation for glycerol esterification
Recovery of triacetin, the triacetate ester of glycerol as biofuel additive.
Reactive distillation configuration for triacetin production using ethylene dichloride as entrainer.