## Slide 1: EKC 464 BIOREFINERY ENGINEERING
Nur Ayshah Rosli, PhD
Room No: 2.22
Ext: 6487

## Slide 2: Separation and purification technologies in biorefinery.

## Slide 3: Affinity-based separation techniques
Adsorption, ion exchange and simulated moving-bed technology for biorefinery applications

## Slide 4: Reference
Separation and purification technologies in biorefineries. Ramaswamy, S., Huang, H. J., & Ramarao, B. V. (2013). John Wiley & Sons Incorporated.
Biorefineries and Chemical Processes: Design, Integration and Sustainability Analysis - Author(s): Jhuma Sadhukhan Kok Siew Ng Elias Martinez Hernandez.

## Slide 5: Adsorption

## Slide 6
Natural gas dehydration plant - Silica Verfahrenstechnik GmbH

## Slide 7: What is adsorption?
A mass transfer process which involves the accumulation of substance at the interface of the two phases, such as, liquid-liquid, gas-liquid, gas-solid, or liquid-solid interface
Adhesion of atoms, ions, or molecules from a gas, liquid, or dissolved solid to a surface
ADSORBATE - the substance which is adsorbed on the surface
ADSORBENT the substance on which surface the adsorbate is adsorbed

## Slide 8
Examples in your daily life?

## Slide 9
ADSORPTION is a spontaneous process
ADSORPTION is an exothermic process

## Slide 10: Adsorption In Liquid
A molecule in the interior of a liquid is, completely surrounded by other molecules so, on the average, it is attracted equally in all directions. On a molecule in the surface, however, there is a resultant attraction inwards, because the number of molecules per unit volume is greater in bulk of the liquid than in the vapour, this gives rise to surface tension. Hence, particles at surface and particles at the bulk are in different environment thus giving rise to difference in free energy at the surface & in the bulk.

## Slide 11: Adsorption in Solids
The Cleavage of a big crystal of solid into smaller units is done to increase surface area . Due to cleavage of a big crystal into smaller unit, residual forces or vacancies gets generated on the surface of the solid. Occupancy of these vacancies by some other molecular species results into adsorption

## Slide 12: Adsorption mechanism

## Slide 13: Two types of adsorption
Physisorption
van der Waals interaction between the adsorbate & the substrate.
Examples , A dispersion or dipolar-dipolar interaction .
Van der Waals interactions are long range but are weak.
Energy released when a particle is physisorbed is of the same order of magnitude as the enthalpy of condensation .
Such small energies can be absorbed as vibrations of the lattice & dissipated as thermal motion, & a molecule bouncing across the surface will gradually lose all its energy & finally adsorb to it.

## Slide 14
Chemisorption
The molecules or atoms stick to the surface of adsorbent by forming a chemical bond (usually covalent) and tend to find sites that maximize their coordination number with the substrate.
The distance between the surface & the closest adsorbate atom is also typically shorter for chemisorption.
A chemisorbed molecule may be torn apart at the demand of the unsatisfied vacancies of the surface atoms, & the existence of molecular fragments on the surface as a result of chemisorption is one reason why solid surface catalyse reactions.

## Slide 15: Difference between physisorption and chemisorption
Physical Adsorption | Chemical Adsorption
Not very Specific | Highly Specific
No electron transfer although polarization of adsorbate may occur | Electron transfer leading to bond formation between adsorbate & adsorbent
Rapid, non-activated & reversible | Activated , may be slow & irreversible
No dissociation of adsorbed species | May involve dissociation
Monolayer or Multilayer | Monolayer only
Only significant at relatively low temperatures | Possible over a wide range of temperatures
Enthalpies are in the region of -20 kJ/mol | Enthalpies are in the region of -200 kJ/molWith the increases in temperature
As the temperature increases, process of Physisorption decreases | Chemisorption first increases & then decreases

## Slide 16: Factors affecting adsorption
Temperature
Adsorption is an exothermic process. Therefore in accordance with Le Chatelier's principle, the magnitude of adsorption should increase with decrease in temperature. It is in the case of physical adsorption . Chemical adsorption first increases with rise in the temperature and then starts decreasing
Pressure
With increase of pressure, adsorption increases up to certain extent till saturation level is achieved - no more adsorption takes place no matter how high the pressure applied.
Surface area
It’s a surface phenomenon therefore adsorption capacity of adsorbent increases with increase in its surface area. Smaller the size of particles of solid adsorbents more is the extent of adsorption at its surface interface
Activation of solid adsorbent
Activation of adsorbent surface done so as to provide more vacant sites on surface. This can be done by breaking solid crystal in small pieces, breaking lump of solid into powders or sub- dividing the adsorbent

## Slide 17: Adsorption isotherm
Adsorption process is usually studied through graphs known as Adsorption Isotherm. The amount of adsorbate on the adsorbent as a function if its pressure (gas) or concentration (liquid) at constant T
Graph between the amounts of adsorbate (x) adsorbed on the surface of adsorbent (m) and pressure at constant temperature
Freundlich
Temkin
Langmuir
BET

## Slide 20: Type of adsorbent
Oxygen Containing Compounds Typically Hydrophilic & Polar Examples : Silica Gel & Zeolites
Carbon Based Compounds Typically Hydrophobic & Non-Polar Examples : Activated Carbon & Graphite

## Slide 21: Activated carbon
Adsorbent: Virtually every solid surface has the capacity to adsorb solutes. From the wastewater/water treatment point of view activated carbon (AC) is the adsorbent of choice. AC prepared from many sources for example, biomass.
These raw materials are pyrolyzed at high temperature under low oxygen conditions (so we don’t get complete combustion). This forms a “char”. The char is then activated by heating to 300 – 1000 oC in the presence of steam, oxygen or C02.
Result: “Activated carbon” which is highly porous, micro-crystalline material which resembles graphite plates with some specific functional groups (e.g. COOH, OH)

## Slide 22
Increasing magnification

## Slide 23: Fixed-bed adsorption system
How will the OUTLET concentration as a function of TIME look like?

## Slide 25: Fluidized-bed system

## Slide 26: Pressure swing adsorption process
The pressure swing adsorption process works at basically constant temperature and uses the effect of alternating pressure and partial pressure to perform adsorption and desorption.
short cycles within the range of minutes
Adsorption is carried out at high pressure (and hence high respective partial pressure) typically in the range of 10–40 bar until the equilibrium loading is reached
regeneration is accomplished by lowering the pressure to slightly above atmospheric pressure resulting in a respective decrease in equilibrium loading.
Application – purification of hydrogen; separation of carbon dioxide from methane by adsorption/desorption of carbon dioxide on zeolites or activated carbon at different pressure levels.

## Slide 27: Temperature swing adsorption process
For a fixed partial pressure, the sorption capacity is high at low temperatures (adsorption) and low at high temperatures (regeneration)
TSA processes use much longer cycles since it takes a considerable amount of time (hours or days) to heat up tons of adsorbent material packed in the vessels
Energy intensive
Commonly used for the trace separations and not for the bulk separations such as ethanol
Example: Recovery of 1-butanol from an acetone-butanol-ethanol (ABE) fermentation broth using temperature-swing adsorption (TSA) technology; Carbon dioxide capture

## Slide 28: Application of adsorption in Biorefinery
Ethanol dehydration
Biodiesel purification

## Slide 29: Adsorption - Ethanol dehydration
In a typical ethanol fermentation, broth containing dilute aqueous solution of about 5–12 wt% ethanol is produced.
Separation of ethanol from this dilute solution accounts for a large fraction of the total production cost.
Distillation is found to be an effective separation process to concentrate the dilute solution up to 85 wt%.
To go above this concentration, distillation becomes expensive requiring high reflux ratios and additional equipment.

## Slide 32
Various technique to break the azeotrope and produce anhydrous ethanol
adsorption, chemical dehydration, dehydration by vacuum distillation, azeotropic distillation, extractive distillation, membrane processes and diffusion distillation
Vapor phase adsorption of water
Potential adsorbent - molecular sieves, lithium chloride, silica gel, and activated alumina, and bio-based adsorbents such as corn grits.
Adsorption is particularly attractive because of its low energy consumption
Anhydrous - (of a substance, especially a crystalline compound) containing no water.

## Slide 33
There are two adsorption techniques used in ethanol-water separation:
liquid-phase adsorption of water from the fermentation broth
vapor-phase adsorption of water from the process stream coming out of distillation column

## Slide 34: Potential adsorbent
molecular sieves
corn grits
activated alumina
lithium chloride
silica gel

## Slide 35: Why industries need dehydrated alcohol
The removal of water from ethanol is ideal for blending with gasoline
The largest consumer of anhydrous ethanol is the oil and gas/fuel ethanol industry
The addition of ethanol to gas helps reduce vehicle exhaust emissions, which, in turn, decreases the release of greenhouse gases such as carbon dioxide and carbon monoxide into the atmosphere.
Anhydrous ethanol is miscible in almost all ratios with gasoline, making it more suitable for this application than hydrous ethanol.
used extensively in the medical industry. Prescription alcohol (at least 98% ethanol by volume) is injected into nearby nerve tissues to relieve symptoms of chronic pain.
specialty chemical industry - in synthetic organic reactions due to its low toxicity and ability to dissolve non-polar substances.

## Slide 36
Double set of molecular sieve beds with a daily dehydration capacity of 1.3 million liters ethanol.

## Slide 37: Biodiesel purification
Biodiesel is an alternative fuel source to standard petrochemical diesel. It is derived from tricylglycerides of either vegetable or animal fat sources.
Triglycerides are reacted with an alcohol (usually methanol, but sometimes ethanol or other alcohols) in the presence of a catalyst to produce biodiesel, or fatty acid esters (usually methyl esters).
The reaction also produces glycerin, which must be separated from the biodiesel.
After the separation process, biodiesel contains several contaminant materials such as soaps and traces of catalyst, along with ionic salts, which are detrimental to the quality of the fuel and thus must be eliminated from the product.
The elimination of water-soluble portion of these materials is usually accomplished by water washing the biodiesel. However, with this method, the water-insoluble impurities remain in the biodiesel. There are also environmental concerns regarding the effluent water.
Magnesol D60 (a synthetic magnesium silicate) - remove both the water-soluble and water-insoluble contaminants such as soaps, free glycerin, free fatty acids, di-glycerides, monoglycerides, and sulfur.
Silica gel is also found to be an efficient adsorbent for removal of glycerol and free fatty acids (FFA) from biodiesel

## Slide 38: Advantage of adsorption
simplicity
low installation cost
environmentally friendly
low energy usage

## Slide 39: Challenges of adsorption in biorefinery
Can you list it?

## Slide 40
The main disadvantage of adsorption is the formation of a secondary waste, such as the spent adsorbent, unusable recovered organic compounds, and organics in the waste water if steam is used for regeneration. Secondary waste may require off-site treatment or specialist disposal
Regeneration - expensive, not straightforward, and results in loss of the adsorbent
The cost of adsorbent - the higher the quality the greater the cost

## Slide 41: Regeneration technique
The reactivation or the regeneration of adsorbents involves restoring the adsorptive capacity of saturated adsorbents by desorbing adsorbed contaminants on the adsorbents surface.
Common technique - thermal reactivation
Step involves (for example; regeneration of activated carbon):
adsorbent drying at approximately 105 °C;
high temperature desorption and decomposition (500–900 °C) under an inert atmosphere; and
residual organic gasification by an oxidizing gas (steam or carbon dioxide) at elevated temperatures (800 °C).

## Slide 42
BUT!
Per adsorption-thermal regeneration cycle between 5 and 15 wt % of the carbon bed is burnt off, resulting in a loss of adsorptive capacity
Thermal regeneration is a high energy process due to the high required temperatures, making it both an energetically and commercially expensive process
Need to be sent elsewhere for efficient regeneration

## Slide 43
Current alternative regeneration methods are:
chemical and solvent regeneration
microbial regeneration
electrochemical regeneration
ultrasonic regeneration
wet air oxidation.

## Slide 44: Research needs and prospects
Further improvements to make adsorption technology commercially feasible
Developing new adsorbents - (i) better selectivity for specific adsorbate, (ii) better stability under biorefinery process conditions, (iii) favorable geometries, and (iv) lower production cost.
Process improvements - using non-conventional ways to regenerate adsorbents such as sonic/ microwave energy can reduce the adsorption/desorption cycle time.
The need for robust predictive model tools.
The need to generate and compile multicomponent adsorption data – for example separation of component from complex fermentation broth
Effective ways to dispose of spent adsorbents.

## Slide 45: Ion Exchange

## Slide 46: Fast revision
What is ion?
What is cation?
What is anion?
Ion - An atom or molecule with a net electric charge due to the loss or gain of one or more electrons.
Cation - a positively charged ion
Anion - a negatively charged ion

## Slide 47
Biodiesel purification with ion-exchange resin

## Slide 48: Principle of Ion Exchange
Adsorption phenomenon where the mechanism of adsorption is electrostatic. Electrostatic forces hold ions to charged functional groups on the surface of the ion exchange resin. The adsorbed ions replace ions that are on the resin surface on a 1:1 charge basis.

## Slide 49: Advantages
in principle, all ions or ionizable species can be removed from aqueous liquids;
recovery of valuable species is possible;
high efficiency;
a large variety of specific resins are available

## Slide 50: Disadvantages
prefiltration is required (suspended particles in the feed should be less than about 50 mg/L to prevent plugging);
interference of competing cations in the wastewater;
low-temperature resistance of organic (resin) ion exchangers

## Slide 51: Properties of ion-exchangers
Degree of cross-linking and porosity
Exchange capacity - represents the number of active sites that are available
Stability and service life - The chemical stability of the matrix, thermal stability of active groups, mechanical stability, osmotic stability, and resistance to drying
Density - hydrodynamic behavior in counterflow systems
Particle size - compromise between the speed of the exchange reaction (which is greater with small beads) and high flow rates (which require coarse particles to minimize the head loss)
Moisture content - Ion-exchange resins carry both fixed and mobile ions, which are always surrounded by water molecules located in the interior of the resin beads.

## Slide 52
Degree of cross-linking and porosity
Resins with a higher degree of cross-linking show more resistance to oxidizing conditions that tend to de-crosslink the polymer.
Activation becomes difficult because access to the interior of the bead is hindered by the high density of the matrix.
The rate of exchange increases in proportion to the mobility of the ions inside the exchanger bead.
If the structure is too dense, ionic motion is slowed down, thus reducing the operating capacity of the resin.
The greater the ionic mobility in the resin the poorer is the differentiation between the adsorption of ionic species with the same charge.
Consequently, the degree of cross-linking in the resin must be increased when greater differences in ionic affinity are required.

## Slide 53: Resin Density
Resin | Density range
strongly acidic cation exchangers | 1.18–1.38 kg/m3
weakly acidic cation exchangers | 1.13–1.20 kg/m3
strongly basic anion exchangers | 1.07–1.12 kg/m3
weakly basic anion exchangers | 1.02–1.10 kg/m3

## Slide 54: Type of Ion Exchanger
Natural: Proteins, Soils, Lignin, Coal, Metal oxides, Aluminosilicates (zeolites) (NaOAl2O3.4SiO2).
Synthetic zeolite gels and most common -polymeric resins (macroreticular, large pores).

## Slide 55
Polymeric resins are made in 3-D networks by cross-linking hydrocarbon chains. The resulting resin is insoluble, inert and relatively rigid. Ionic functional groups are attached to this framework.

## Slide 56: Cation Exchanger
It possesses negatively charged groups and these will attract positively charged groups.

## Slide 57: Anion Exchanger
It has positively charged groups, which will attract negatively charged molecules.

## Slide 59: Commercial ion-exchange resins
Ion-exchange resins are made by the combined polymerization of styrene and divinylbenzene, which leads to the generation of “gel”-type resins with limited porosity to the molecular dimensions
Resins are classified based on the type of functional group they contain and their % of cross-linkages
strong acid cation resins
weak acid cation resins
strong base anion resins
weak base anion resins

## Slide 60: Strong acid cation resin
Strong acid cation resins contain sulfonic radicals (represented by R-SO3 –H+, sulfonated polystyrene) whose hydrogen ion can be exchanged with other cations.
This is the resin of choice for almost all softening applications.
These strong acid exchangers operate at any pH, separate all salts, and require substantial amounts of regenerant.
Structure of strong acid cation resin (sulfonated polystyrene resin)

## Slide 61: Weak acid cation resins
Weakly acidic – functional groups derived from weak acids, e.g., R-COOH (carboxylic).
Weak acid cation resins contain caboxilic radicals (represented by R-CO2 –H+) whose hydrogen ion can be exchanged with cations that are linked to weaker anions than acetic acid such as carbonates and bicarbonates.
Highly efficient, but is subject to reduced capacity from increasing flow rate, low temperatures, and a hardness-to-alkalinity ratio below 1.

## Slide 62: Strong base anion resins
Strong base anion resins contain quaternary ammonia radicals (represented by R–N(CH3)3+OH–) whose OH– is exchangeable with other anions.
strong base anion resins can be divided into two main groups: type 1 (exchange sites have three methyl groups) and type 2 (the ethanol group replaces one of the methyl groups).
Type-1 resins are more resistant to high temperatures than type 2 resins and should be used on highly alkaline and high silica waters
Structure of strong base anion resin (chloro-ammonia resin)

## Slide 63: Weak base anion resins
Weak base anion resins contain radicals of secondary or tertiary amines, which only exchange their OH– with the anions of quite weak acids, such as carbonic or silicic acids.
The polyamine functional group acts as an acid adsorber, removing strong acids from the cation effluent stream.
This type of resin should be used on waters with high levels of sulfates and chlorides.

## Slide 65: Physical properties of resins
Particle size: 50-200 mesh fine powder, should allow free flow of mobile phase, should contain more exchangeable functional groups
Cross linking & swelling: When more cross-linking agent is present, they are more rigid, but swells less.
When swelling is less, separation of ions of diff sizes is difficult as they can’t pass through the pores present. When less cross-linking agent is present, they are less rigid, but swell more
Separation will not be efficient as exchange of functional groups does not take place due to wide pore
Hence an optimum quantity of cross-linking agent should be added to the polymeric ion exchange resin for the separation to be effective.

## Slide 66: General application of ion exchange
Water softening - In water softening by ion exchange, calcium and magnesium cations are exchanged with Na+ or H+ cations.
Hard water - presence of calcium and magnesium cations
Why industrial processes requiring softened water?
preparation of feed water for steam boilers to prevent scaling
treatment of water used for cooling containers after thermal processing to prevent unsightly “spots” left after the water drops dry out
preparation of softened process water for the production of beverages, for cooking legumes, and so forth.

## Slide 67
Other application
Total removal of electrolytes from water
Removal of nitrates in water
Application in food industries
Decolorization of edible oils with “bleaching earths” (activated clays)
Decolorization of sugar syrup with activated carbon in the manufacture of sugar
Removal of bitter substances from fruit juices by adsorption on polyamides
Odor abatement by passing gaseous emanations through activated carbon
Removal of chlorine from drinking water by adsorption on carbon

## Slide 68: Application in chromatography
What is chromatography?
HPLC (High Performance Liquid Chromatography)?
GC (Gas chromatography)?

## Slide 69: Chromatography
physical method of separation in which the components of a mixture are separated by their distribution between two phases
one of these phases in the form of a porous bed, bulk liquid, layer or film is generally immobile (stationary phase)
while the other is a fluid (mobile phase) that percolates through or over the stationary phase.
widely used separation technique in chemical laboratories, where it is used in analysis, isolation and purification, and it is commonly used in the chemical process industry as a component of small and large-scale production.

## Slide 70
The various constituents of the mixture travel at different speeds, causing them to separate.
Ion exchange chromatography has a wide range of uses for the purification of antibiotics from fermentation medium.

## Slide 71
The general components of a chromatographic system, as illustrated here by using a column to separate two chemicals, A and B.

## Slide 72: Mode of Operation: Elution chromatography
As a sample's components pass through this system, the components that have the strongest interactions with the stationary phase will be more highly retained by this phase and move through the system more slowly than components that have weaker interactions with the stationary phase and spend more time in the mobile phase.

## Slide 73: Other example using chromatography
Separation of fructose from its mixture with glucose generated during the hydrolysis of saccharose.
Separation of amino acids from sugar industry or animal wastes

## Slide 74: Application
Biodiesel bioefineries

## Slide 75: Biodiesel biorefineries using ion exchange separation
Biodiesel contains impurities like methanol, glycerin, glycerides, metals and soap. Use ion exchange in dry washing of these impurities.
Dry washing - Adsorbents consist of acidic and basic adsorption (binding) sites and have strong affinity for these polar compounds.
Dry washing is usually carried out at a temperature of 65˚C and the process is mostly completed within 20–30 min.
This permits the amount of glycerides and total glycerol in crude biodiesel to be lowered to a reasonable level during the washing process.

## Slide 76: Biodiesel biorefineries using ion exchange separation
Advantages in the use of ion exchange in dry washing:
the high affinity for polar compounds present in biodiesel
it is a waterless process that is quicker than water-washing processes
it is easy to incorporate in industrial plants
it is easy to install
No wastewater is generated and the solid waste can be used

## Slide 77: Application
Ion exchange in lignocellulosic bioefineries
detoxification of fermentation hydrolyzates in the conversion of cellulosic biomass to fuel ethanol
purification of succinic acid where the ion exchangers make the acidification with a simultaneous crystallization process

## Slide 78: Regeneration
Spent or exhausted columns must be regenerated because of the cost of the resin would make one-time use prohibitive. Since ion exchange is a very reversible process regeneration can be accomplished by manipulation of solution composition.

## Slide 79: Regeneration
The ion exchange resin after separation may not be useful for next separation as exchangeable functional groups are lost
But due to cost of the ion exchange resins they cannot be disposed off
Hence reactivation, regeneration
Regeneration makes the used ion exchange resin to be as efficient as a virgin resin.
Regeneration: replacement of the exchangeable cations or anions present in the original resin
Hence regeneration of the cation exchange resin is done by the charging the column with strong acid like HCl

## Slide 80: CASE STUDY – Pair Activity
With your partner, discuss:
Recovery of succinic acid from fermentation broth using ion exchange
Q1. What type of resin may be needed for recovery of succinic acid?
Q2. Suggest what kind of impurities exist in fermentation broth?
Q3. Draw a schematic diagram of ion exchange column(s) for separation of succinate from fermentation broth, showing input and output line/arrow.
Q4. What is the process that may required to purify the succinic acid to 99.9% purity?

## Slide 81: Answer – Case study
Anion exchange resins can be used to recover succinic acid from fermentation broth.
The succinic acid solution is passed through ion exchange columns. The succinate is adsorbed in the resin and converted into the acid form during regeneration of the ion exchange resin.
Regeneration of the resin involves water washing to remove unbounded material followed by washing with an acid solution to recover succinic acid.
The process is selective towards succinic acid and allows separation from other organic acids (e.g., acetic acid and lactic acid).
The succinic acid is purified by crystallization to produce succinic acid with purity higher than 99%.

## Slide 82
Operation of ion exchange columns at (a) start-up, (b) cleaning and (c) regeneration.

## Slide 83: Simulated Moving-Bed

## Slide 84: What is SMB?
SMB is Simulated Moving Bed Chromatography.
SMB is continuous countercurrent chromatography. The feed is pumped into the system and two (or more) product streams are continuously collected.
SMB has been used to produce millions of tons of bulk commodities (p-xylene, high fructose corn syrup, etc...) for the past four decades.
Due to improvements in column and equipment technology, SMB has recently been used in the pharmaceutical industry (Sandoz, SmithKline, UCB, Pfizer).
  HPLC costs: $100/kg to $5000/kg
  SMB costs: $50/kg to $200/kg

## Slide 85
The SMB process enables the separation of binary mixtures by means of a simulated countercurrent between the solid and liquid phases.

## Slide 86: SMB versus chromatography
Advantages of SMB:
  Lower solvent utilization (up to 10 times less than batch HPLC) - the solvent is automatically recycled
  Generally can use less expensive, larger stationary phases
  Able to get high recovery and high purity
  Sometimes better productivity
  Lower labor and QC costs - significant cost savings
  Only partial separation of solutes is required to obtain high purity.
  Higher yield than batch – 10% more than batch.
  High throughput – 5 to 10-fold increase.
  Lower solvent consumption – An order of magnitude lower.
  Continuous process.
  reduces floor space, equipment size, and manpower
Disadvantage of SMB:
  Binary separation only
  Complexity – more complex design

## Slide 87
Basic Principle
Mobile Phase
Feed
Continuous Countercurrent Chromatography
stationary column
A sample is injected in the centre of a stationary column
The two components move at different speeds and are separated
If we now move the column from right to left, at a speed halfway
between that of the solutes, they now move in different directions ...

## Slide 88
Basic Principle
Mobile Phase
Feed
column
The two solutes now move in different directions relative to a stationary
observer. If the column is very long, the bands will continue to separate.
Continuous Countercurrent Chromatography

## Slide 89
Basic Principle
Mobile Phase
Feed
column
If we continue to add sample at the center, the components will continue
to separate
Continuous Countercurrent Chromatography

## Slide 90
This is clearly a continuous system, but there are problems.
The column needs to be of infinite length, the actual moving of solids is
very difficult and some way to introduce and remove the sample and the
products are needed.
We solve this by cutting the column into small segments and simulating
the moving of them
Basic Principle
Mobile Phase
Feed
column
Continuous Countercurrent Chromatography

## Slide 91
The feed and solvent inlets are now placed between the segments
and are moved each time a segment is moved from one end to the other
Basic Principle
Mobile Phase
Feed
column
Continuous Countercurrent Chromatography

## Slide 92
Products are removed by bleeding off a carefully calculated flow
at suitable exit points. This changes the velocity of the bands in
the column and forces the products to move toward the ports
This ensures that the column segments are clean before they are moved
and that the solvent can be recycled directly back through the system
Mobile Phase
Basic Principle
Mobile Phase
Feed
column
Continuous Countercurrent Chromatography

## Slide 93: SMB – Method Development
Start with linear batch experiments
Increase either mass or volume of load to overload the column
Calculate isotherm
Determine resistance to mass transfer (if important)
Calculate necessary flow rates
Optimize (either on-the-fly or with a proven model)

## Slide 94: SMB Optimization
Independent variables:
  Flow rates
    Recycle, Desorbent, Raffinate, Extract, Feed
  Period (switching time)
  That’s it.
Procedure:
  Get the system bound, manipulate the flow rates to maximize throughput at required purity

## Slide 95: Commercial Applications of SMB
Hydrocarbons
Sugars
Agrochemicals
Antibiotics
Peptides
Chiral Drugs
  Gaining tremendous momentum – FDA approves of the technology
  Chiral resin manufacturers sell resins specifically made for SMB
Proteins?
  Useful as polishing step?
    SEC: remove aggregated form of product
  Multicomponent separations more difficult than traditional uses
    8, 12, even 16 zone systems being examined

## Slide 96
Schematic diagram of SMB operation in the simplified bioethanol production from biomass

## Slide 97: Five-zone SMB for sugar isolation from dilute-acid hydrolysate
Dilute acid is first used to hydrolyze (or pretreat) the hemicellulose in biomass.
The more recalcitrant cellulose residue is then separated from the hydrolysate.
The primary hydrolysate components are six sugars (glucose, xylose, cellobiose, galactose, arabinose, and mannose) and four impurities (sulfuric acid, acetic acid, hydroxymethyl furfural, and furfural).
These impurities inhibit downstream fermentation and must be removed in a purification step.
After purification, the purified hydrolysate is added back to the solid residue for simultaneous enzymatic hydrolysis of the cellulose and fermentation of the sugars to ethanol.

## Slide 98: Other application in biorefineries
purification of lactic acid in fermentation broth
purification of glycerol by-product from biodiesel processing
separation of sugar hydrolysate and concentrated sulfuric acid